## Slide 1: Exercises – biological signals
Exercise 12 - SS 2014 – Michel Kana

## Slide 2: What will we do today?
Introduction to Wavelet Transform
Heart rate variability with Wavelet Transform
Summary

## Slide 3: Fourier Transform vs. Wavelet Transform
Fourier analysis represents a signal as either a function of time or frequency, but not both.
Like sines and cosines in Fourier analysis, wavelets are used as basis functions in representing other functions.
Wavelets are waveform of limited duration that has an average value of zero.
Wavelets are located in both frequency (via dilation) and time (via translation) domains.

## Slide 4: Wavelets
Wavelets are generated from a single basic wavelet called mother wavelet as follows: , where is the shift-coefficient and is the scale coefficient.
Haar wavelet
Prominent examples are the Haar and Daubechies wavelets
Daubechies wavelets

## Slide 5: The Wavelets Transform
Wavelet Transform is the representation of a signal as a linear combination of wavelet basis functions:
A wavelet basis consists of a father wavelet that represents the smooth baseline trend and a mother wavelet that is dilated and shifted to construct different levels of detail.
The wavelet basis functions are chosen according to the signal being approximated.
Step1: take a wavelet and correlate it with a section of the signal
Step2: shift the wavelet to the right and repeat step 1 until the whole signal is covered
Step3: scale (stretch) the wavelet and repeat steps 1 and 2

## Slide 6: Example of wavelet transform

## Slide 7: Example of wavelet transform
Haar wavelet
shift
scale

## Slide 8: The Wavelet Transform in Matlab
F1 = 10; F2 = 40; Fs = 1000; t = 0:1/Fs:1; x = sin(2*pi*t*F1) + sin(2*pi*t*F2); clf; plot(x,'r'); axis tight title('Signal'); xlabel('Time or Space')
Consider the following data x with two component frequencies components
Sample frequency (Hz)
10 Hz component
40 Hz component

## Slide 9: The Wavelet Transform in Matlab
wname = 'gaus4'; scales = 1:1:128; TAB_Sca2Frq = scal2frq(scales,wname,1/Fs); [~,idxSca_1] = min(abs(TAB_Sca2Frq-F1)); Sca_1 = scales(idxSca_1) [~,idxSca_2] = min(abs(TAB_Sca2Frq-F2)); Sca_2 = scales(idxSca_2)
Wavelet name
scales
table of scales and frequencies
The scalogram is a visual method of displaying a spectrum of frequencies over time.
There are 3 axes: x representing time, y representing scale, and z representing wavelet coefficient value
Scale for frequency F1
Scale for frequency F2
Using the function scal2freq, we compute the correspondence table of scales and frequencies for the gaus4 wavelet.
Then, we find the scales corresponding to the frequencies F1 = 10 and F2 = 40.

## Slide 10: The Wavelet Transform in Matlab
clf; coefs = cwt(x,scales,wname,'scalCNT'); hold on plot([1 size(coefs,2)],[Sca_1 Sca_1],'Color','m','LineWidth',2); plot([1 size(coefs,2)],[Sca_2 Sca_2],'Color','m','LineWidth',1);
Wavelet coefficients
coefs = cwt(x,scales,'wname‘,’scalCNT’) computes the continuous wavelet transform (CWT) coefficients
of the real-valued signal x at real, positive scales, using wavelet 'wname' and
displays a contour representation of the scalogram
Highlight frequency component F1
Highlight frequency component F2

## Slide 11: The Wavelet Transform in Matlab
clf; wscalogram('image',coefs,'scales',scales,'ydata',x); hold on plot([1 size(coefs,2)],[Sca_1 Sca_1],'Color','m','LineWidth',2); plot([1 size(coefs,2)],[Sca_2 Sca_2],'Color','w','LineWidth',1);
Wavelet scalogram
wscalogram('image',coefs,'scales',scales,'ydata',x) computes the scalogram SC which represents
the percentage of energy for each coefficient.
Highlight frequency component F1
Highlight frequency component F2

## Slide 12: Heart rate variability with Wavelets Transform
Discrete WT can be performed using a Daubechies 4 wavelet with 6 logarithmically progressing scales
  scale 1 and 2 correspond to 0.5-2 Hz
  scales 3 and 4 correspond approximately to HF (0.125 –0.5 Hz)
  scales 5 and 6 correspond to LF (0.03125 – 0.125 Hz).
http://www.mathworks.com/help/wavelet/examples/wavelet-scalogram-using-1d-wavelet-analysis.html

## Slide 13: Exercice 1: RR Interval measurement with BIOPAC
Biopac MP35 measurement system
  ECG is recorded using Biopac SS2L wires plugged in the first channel.
Biopac Student Lab PRO software
  The acquisition is set up at a sampling rate of 200 Hz.
  Analog Channel CH1 should have the preset ECG (.5 - 35 Hz).
  Calculation Channel C1 should have the preset ECG – RR Interval

## Slide 14: Heart Rate Variability with Matlab
Fs = 4; x = resample (RR, Fs, 200) clf; plot(x,'r'); axis tight title('Signal'); xlabel('Time or Space')
Resample from 200 Hz to 4 Hz
Importing RR intervals from Biopac into Matlab
  File -> Save as text

## Slide 15: Heart Rate Variability with Matlab
wname = 'gaus4'; scales = 1:1:128; TAB_Sca2Frq = scal2frq(scales,wname,1/Fs); LF = (0.15-0.04)/2; HF = (0.4-0.15)/2; [~,idxSca_1] = min(abs(TAB_Sca2Frq-LF)); Sca_1 = scales(idxSca_1) [~,idxSca_2] = min(abs(TAB_Sca2Frq-HF)); Sca_2 = scales(idxSca_2)
Wavelet name
scales
table of scales and frequencies
Scale for LF frequency 0.04 – 0.15 Hz
Scale for HF frequency 0.15 – 0.4 Hz

## Slide 16: Heart Rate Variability with Matlab
clf; coefs = cwt(x,scales,wname,'scalCNT'); hold on plot([1 size(coefs,2)],[Sca_1 Sca_1],'Color','m','LineWidth',2); plot([1 size(coefs,2)],[Sca_2 Sca_2],'Color','m','LineWidth',1);
Wavelet coefficients
Highlight LF frequency component
Highlight frequency HF component

## Slide 17: Heart Rate Variability with Matlab
clf; wscalogram('image',coefs,'scales',scales,'ydata',x); hold on plot([1 size(coefs,2)],[Sca_1 Sca_1],'Color','m','LineWidth',2); plot([1 size(coefs,2)],[Sca_2 Sca_2],'Color','w','LineWidth',1);
Wavelet scalogram
Highlight LF frequency component
Highlight HF frequency component

## Slide 18: Exercice 2: HRV with wavelet transform during breathe holding
Procedure
  Subject is instrumented for ECG measurement with Biopac.
  Take a couple minutes relaxation before the experiment
  Perform a 1 min recording in a sitting position while breathing normally.
  Perform another recording while the subject exhales and empties the lungs; then immediately holds breathing as long as possible.
  Perform another 1 min recording while breathing normally
Evaluation
  Export the data from BSL Pro as txt File (Edit Clipboard Copy Wave Data).
  Import the data into Matlab using tdfread or csvread
  Estimate the total power of each frequency band (LF and HF) using Matlab wavelet transform functions: cwt, waveinfo, scal2frq, wscalogram.
    Reveal the change in the power of HF component over the time

## Slide 19: Exercice 3: HRV with wavelet transform during active standing
Procedure
  Subject is instrumented for ECG measurement with Biopac.
  Perform a 1 min recording in a sitting position.
  Perform another 1 min recording while the subject actively stands up from the sitting position.
  Perform a 1 min recording in a sitting position.
Evaluation
  Export the data from BSL Pro as txt File (Edit Clipboard Copy Wave Data).
  Import the data into Matlab using tdfread or csvread
  Estimate the total power of each frequency band (LF and HF) using Matlab wavelet transform functions: cwt, waveinfo, scal2frq, wscalogram.
    Reveal the change in the power of HF and LF components over the time

## Slide 20: Team Projects
Project 1: Cardiovascular Signal Analyzer
  Digital filtering of a raw PPG signal
  Extraction of PH (pulse height) and PP (peak-to-peak) values from a filtered PPG signal
  MAP estimation using PH
  Fourier transform of PP intervals and estimation of HF and LF
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency, signal type (ECG or PPG or both) and channel numbers
    User should be able to filter the raw signal
    User should be able to execute PP, PH, MAP, LF, HF computation
    User should be able to display plots of the raw signal for a given start and end timestamp
    User should be able to display plots of PP, PH, MAP over the time for a given start and end timestamp and display the value of LF and HF

## Slide 21: Team Projects
Project 2: Nervous Activity Analyzer
  Digital filtering of a raw EEG signal
  Extraction of alpha, beta, theta, delta waves from a filtered EEG signal
  Computation of STD, AVG and CC
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency
    User should be able to filter the raw signal
    User should be able to execute alpha, beta wave, theta, delta wave computation using Fourier or Wavelet transform or digital filtering
    User should be able to execute STD, AVG, CC computation
    User should be able to display plots of the raw signal for a given start and end timestamp
    User should be able to display plots of alpha, beta wave, theta, delta waves over the time for a given start and end timestamp and display the values for STD, AVG and CC

## Slide 23: Team Projects
Project 3: Muscle Activity Analyzer
  Digital filtering of a raw EMG signal
  Computation of rectified EMG from a filtered EMG signal
  Computation of the spectrum of the filtered EMG signal using Fourier transform
  Computation of RMS, ARV
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency
    User should be able to filter the raw signal
    User should be able to execute rectified EMG computation
    User should be able to execute Fourier transform of the rectified EMG for a given start and end timestamp
    User should be able to execute RMS, ARV computation for a given start and end timestamp
    User should be able to display plots of the raw EMG, rectified EMG, EMG Fourier transform for a given start and end timestamp
    User should be able to display the values for RMS, ARV for a given start and end timestamp