## Slide 1: Exercises – biological signals
Exercise 4 - SS 2014 – Michel Kana

## Slide 2: What will we do today?
The physiology behind PPG
Structure of the PPG Signal
PPG measurement with BIOPAC
Summary

## Slide 3: The physiology behind PPG
Photoplethysmography (PPG) is an optical measurement technique that can be used to detect blood volume changes in the microvascular bed of tissue
A photodetector can be placed on a tissue’s surface alongside the light-emitting diode and record the light that returns back
Light intensity is attenuated by oxygenated and deoxygenated hemoglobin (in blood cells), myoglobin (in muscle), and cytochromes, as well as melatonin (in skin)
Reductions in light intensity indicate relative increases in blood volume and vice versa
Wiggers diagram

## Slide 4: Structure of the PPG Signal
Waves in the PPG
  The photoplethysmogram waveform consists of one systolic wave and one diastolic wave.
  The second derivative photoplethysmogram waveform consists of four systolic waves (a, b, c, and d waves) and one diastolic wave (e wave).
Ref.: M. Elgendi “Standard Terminologies for Photoplethysmogram Signals”
PPG
2nd derivative of
PPG

## Slide 5: Structure of the PPG Signal
Parameters in the PPG signal
  PH: pulse height or pulse amplitude
  CP: cardiac period
  FWHM: full width half max
  PW: peak width
  PT: peak threshold
  PPT: pulse travelling time

## Slide 6: PPG Measurement
Ref.: http://www.engin.swarthmore.edu/~dluong1/E72/FinalProject/heart.htm
Operational configuration
  Side-by-side mode
  Transmission mode
Noise sources
  Movement artefacts
  Ambient light interference
  Variation in temperature
  power line interference

## Slide 7: Exercice 1: PPG measurement with BIOPAC
Biopac MP35 measurement system
  PPG is recorded using Biopac SS4LA plethysmograph transducer plugged in the first channel.
  Tranducer should be attached to the left hand, index finger.
Biopac Student Lab PRO software
  The acquisition is set up for Recording and Append into Memory at a sampling rate of 200 Hz. The total acquisition length can be set to 1 hour.
  In the Setup Channels menu, the check boxes Acquire Data, Plot on Screen, Enable Value Display are enabled for the first channel.
  Analog Channel CH1 should have the following settings
    AC coupling 0.5 Hz High Pass, 1K Low Pass
    Hardware-based filter 60 Hz Low Pass
    Total gain 5000
  Calculation Channel C1 should calculate the Difference of the channel CH1 in order to estimate the first derivative of the PPG waveform. Channel C1 should not be visible.
  Calculation Channel C2 should calculate the Difference of the channel C1 in order to estimate the second derivative of the PPG waveform
PPG parameters calculation
  Select two consecutive cardiac cycles
  Read the values for PH, CP, FWHM, PW, PT
  Estimate the heart rate
  Estimate arterial stiffness and vascular aging

## Slide 8: Exercice 2: ECG & PPG measurement with BIOPAC
Biopac MP35 measurement system
  PPG is recorded using Biopac SS4LA plethysmograph transducer plugged in the first channel.
  3 leads ECG is recorded using Biopac SS2L connecting wires plugged in the 2nd channel.
Biopac Student Lab PRO software
  Analog Channel CH2 should have the following settings
    AC coupling 0.5 Hz High Pass, 1K Low Pass
    Hardware-based filter 35 Hz Low Pass
    Total gain 2000
  Calculation Channel C3 should calculate the heart rate from the PPG signal
  Calculation Channel C4 should calculate the heart rate from the ECG signal
  Calculation Channel C5 should estimate the mean arterial pressure from the pulse amplitude in the PPG signal
Pulse travel time calculation
  Select one cardiac cycle
  Use the measurement window and calculate the PPT
  Estimate the mean arterial blood pressure using the PPT and the pulse amplitude
  Suggest a method for calculating and displaying the PPT during realtime measurement
Heart rate comparison
  Select a sufficiently long time period
  Calculate and compare the mean, min and max heart rates obtained from ECG and PPG

## Slide 9: Exercise 3: active standing test
Active Change of Posture Test
  Subject is instrumented for PPG measurement with Biopac by the examiner.
  The examiner records the PPG signal for 120 seconds.
  The examiner gives a vocal signal to the subject to stand.
  Subject stands up.
  The examiner records the PPG signal for 120 seconds.
Evaluation
  Identify significant phases in the heart rate and blood pressure waves
  Compare the mean values between phases

## Slide 10: Summary
[What did we learn today]
Physiology behind the photoplethysmogram.
Structure of the PPG signals.
Measurements and signal analysis.
[Plan for the next week]
Respiration measurement & analysis