## Slide 1: Exercises – biological signals
Exercise 9 - SS 2014 – Michel Kana

## Slide 2: Team Projects
Project 1: Cardiovascular Signal Analyzer
  Digital filtering of a raw PPG signal
  Extraction of PH (pulse height) and PP (peak-to-peak) values from a filtered PPG signal
  MAP estimation using PH
  Fourier transform of PP intervals and estimation of HF and LF
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency, signal type (ECG or PPG or both) and channel numbers
    User should be able to filter the raw signal
    User should be able to execute PP, PH, MAP, LF, HF computation
    User should be able to display plots of the raw signal for a given start and end timestamp
    User should be able to display plots of PP, PH, MAP over the time for a given start and end timestamp and display the value of LF and HF

## Slide 3: Team Projects
Project 2: Nervous Activity Analyzer
  Digital filtering of a raw EEG signal
  Extraction of alpha, beta, theta, delta waves from a filtered EEG signal
  Computation of STD, AVG and CC
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency
    User should be able to filter the raw signal
    User should be able to execute alpha, beta wave, theta, delta wave computation using Fourier or Wavelet transform or digital filtering
    User should be able to execute STD, AVG, CC computation
    User should be able to display plots of the raw signal for a given start and end timestamp
    User should be able to display plots of alpha, beta wave, theta, delta waves over the time for a given start and end timestamp and display the values for STD, AVG and CC

## Slide 5: Team Projects
Project 3: Muscle Activity Analyzer
  Digital filtering of a raw EMG signal
  Computation of rectified EMG from a filtered EMG signal
  Computation of the spectrum of the filtered EMG signal using Fourier transform
  Computation of RMS, ARV
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency
    User should be able to filter the raw signal
    User should be able to execute rectified EMG computation
    User should be able to execute Fourier transform of the rectified EMG for a given start and end timestamp
    User should be able to execute RMS, ARV computation for a given start and end timestamp
    User should be able to display plots of the raw EMG, rectified EMG, EMG Fourier transform for a given start and end timestamp
    User should be able to display the values for RMS, ARV for a given start and end timestamp