## Slide 1: PPG Analyzer 9800FX
Timo, Mirva, Miloš

## Slide 2: The team!
Timo Lauteslager BSc. – born in 1990, finished his bachelor in Biomedical engineering, currently part of CEMACUBE programme
Mirva Reijonen – born in 1990, has a bachelor in Chemical engineering, currently in student exchange in Czech Republic
Miloš Kaćanski Ing. – born in 1989, got his degree in Biochemical engineering, currently part of CEMACUBE programme

## Slide 3: PPG
Photoplethysmography (PPG) is an optical measurement technique that can be used to detect blood volume changes in the microvascular bed of tissue

## Slide 4: Structure of the PPG Signal
Parameters in the PPG signal
  PH: pulse height or pulse amplitude
  CP: cardiac period
  FWHM: full width half max
  PW: peak width
  PT: peak threshold

## Slide 5: The project
  Digital filtering of a raw PPG signal
  Extraction of PH (pulse height) and PP (peak-to-peak) values from a filtered PPG signal
  MAP estimation using PH
  Fourier transform of PP intervals and estimation of HF and LF
  Implementation in Matlab, if possible with an interactive GUI
    User should be able to import the raw signal import from a Biopac text export
    User should be able to enter the sampling frequency,
    User should be able to filter the raw signal
    User should be able to execute PP, PH, MAP, LF, HF computation
    User should be able to display plots of the raw signal for a given start and end timestamp
    User should be able to display plots of PP, PH, MAP over the time for a given start and end timestamp and display the value of LF and HF

## Slide 6: The signal
Data for project design was:
  From a superficialy healthy subject treated with Czech culture for last nine months, with some interuptions
  Recorded by Biopack SS4LA plethysmograph transducer
  Exported into text file with Biopack student lab PRO software
  Analysed in Mathlab, version 2011a

## Slide 7: Heart rate estimation
Filtering with a strong FIR low pass filter
  FIR for linear phase characteristics
Peak detection
Removal of small intervalls
  Lower than 0.6 mean interval
Determination of mean Heart rate

## Slide 8: Digital filtering of a raw PPG signal
FIR low pass (experimentaly determined values using Sptool ):
Passband Frequency= 1
Stopband Frequency= 12
Passband Ripple= 0.057
Stopband Attenuation= 0.003
Density Factor= 20

## Slide 9: Extraction of PH (pulse height) and PP (peak-to-peak) values from a filtered PPG signal
Using the filtered data
Peak detection using minimal peak distance
  Minimal peak distance intelligently set after heart rate
Intervals are determined for PP interval
For Pulse height:
  Peak detection of negative signal
  Positive and negative peaks are sorted
  Difference between peak values are calculated
  Removal of all even data

## Slide 10: MAP estimation using PH
*Using mean peak height

## Slide 11: Fourier transform of PP intervals and estimation of HF and LF
Doubling of Fs
Fast Fourier transform of peak to peak intervals
Interpolation of the amplitude spectrum
Integration of HF and LF intervals
  LF: 0.04 – 0.15 Hz
  HF: 0.15 – 0.5 Hz

## Slide 12: Implementation in Matlab
[sound of Matlab opening]

## Slide 13: Discussion
Strengths:
  Every physician can use it without background knowledge
  Low number of mathematical operations -> Fast
  Easily user-adaptable
  User can evaluate peak detection
Possible improvements
  Program is not compatibility-tested with different operating systems and Matlab versions
  Parameters are set after 1 PPG data set, validation with other sets required
  Stand-alone program
  Added functions: HR, PA, MAP, Amplitude spectrum over a user-defined interval

## Slide 14: Questions?